## Slide 1: Bridge Design in AutoCAD Civil 3D
Tony Huang, Abraham Xu, Charles Zuo
SWD
Civil 3D
Notes: Hello everyone, this is Tony Huang. I will introduce a proposed work flow of designing bridge in Civil3D. It’s a report from the bridge research group. The group includes me, Abraham and Charles.

## Slide 2: Agenda
Bridge types & scope
How to design a bridge
What can Civil 3D do in the bridge designing
Overview
Notes: This is the agenda. The focus of this topic will be what Civil3D can do in the bridge designing.

## Slide 3: Bridge Types
Arch Bridge
Suspension Bridge
Cable-stayed Bridge
Continuous Truss Bridge
Notes: First of all I will introduce the bridge types. This is the arch bridge. This kind is named from the arch.
An arch bridge is a bridge with abutments at each end shaped as a curved arch. Arch bridges work by transferring the weight of the bridge and its loads partially into a horizontal thrust restrained by the abutments at either side.
Zhaozhou Bridge, Fredrikstad Bridge Norway腓特烈斯塔（挪威东南部海港）

## Slide 4: Bridge Types
Arch Bridge
Suspension Bridge
Cable-stayed Bridge
Continuous Truss Bridge
Notes: This is the suspension bridge. There are some vertical cables.
A suspension bridge is a type of bridge in which the deck (the load-bearing portion) is hung below suspension cables on vertical suspenders.
Shantou Bridge, Bosphorus Bridge in Istanbul博斯普鲁斯大桥(伊斯坦布尔)

## Slide 5: Bridge Types
Arch Bridge
Suspension Bridge
Cable-stayed Bridge
Continuous Truss Bridge
Notes: This is the cable-stayed bridge. There are one or more towers and some slope cables.
A cable-stayed bridge is a bridge that consists of one or more towers, with cables supporting the bridge deck.
Yangpu Bridge, Rama VIII Bridge (罗摩8)

## Slide 6: Bridge Types & Scope
Arch Bridge
Suspension Bridge
Cable-stayed Bridge
Continuous Truss Bridge
------ Scope
Notes: Truss and Continuous Truss Bridge
This type of bridges likes a bench. It doesn’t have arch curves, has no big towers or cables. All of the loads are through the supports transfer to the ground.
To design a continuous truss bridge is our scope.

## Slide 7: How to design a bridge
Notes: Conceptual design, both model type and structure type of bridge will be selected.
And then the engineer will do some structure analysis, and detailed design, and redesign. Sometime the final design comes out with several iterations.
Make the construction process management plan.
Submit the drawings and the project reports.

## Slide 8: How to design a bridge
Cooperation between road engineer and bridge engineer
Step 1
Step 2
Aim
Design Bridge
Design Road
Save the construction cost
Design Road
Design Bridge
Enhance driving comfort and security
Notes: Another point I have to say, the working way between road engineer and bridge engineer has changed.
In the old way, bridge engineer determine the location where building a bridge first, and then road engineer design a road to adapt to the bridge. (Sometime this way is still used, when designing the especially large bridge.) It is in order to save the construction cost.
But now, more and more is designing road at the first, and then set up bridge. It is in order to enhance driving comfort and security.

## Slide 9: Proposed Work Flow in Civil 3D
Civil3D
Modeling
Alignment
Profile
Assembly
Bridge
Section
Road
Section
Corridor
Intersection
Supports
Foundation
SAC
Drawings & Reports
Structure
Analysis
(RSA)
(RST)
(ASD)
Design conditions
Gravity load
Wind load
Shock
Brake load
Mechanics
Compressive
Bending
Shearing
Material
Steel
Reinforced concrete
PresTrussed concrete
Foundation design
...
...
...
...
Work Flow Demo
Notes: This is the proposed work flow of designing bridge. It is similar to designing a road. In the left picture, the yellow parts are newly added, as Bridge section, Supports, Foundation and Piles. And these three parts are needed to do structure analysis. And we also should improve the function of corridor and intersection. I will talk about them detail in the following pages.

## Slide 10
Alignment
Profile
Notes: First of all, the road engineer will design an alignment and profile as designing a normal road. And then the bridge engineer will get the data from the road design. In the profile, parts of them will be marked as bridges.
Any way the profile can be separated from the ground, so it will be more gently.

## Slide 11
Assembly
Bridge
Section
Notes: Here are some types of the bridge sections.
The first one is an independent box-girder while has both arc sides. This type is usually used in city, because it’s modeling beautiful.
The second one is an I-Beam. The material of this one is concrete, and some of I-Beam is steel. The coverage in the above of I-Beam is the concrete slab.
The last one is another type of box-girder, which is made up by many boxes. And these can be made in the factory, and then transported to the location and installing.
By the way, in the section, the balustrades are indispensable.

## Slide 12
Assembly
Road
Section
Notes: And then add the road section on the top of the bridge section. And it is simple than the normal road designing, because don't need to design Shoulders, Daylight.

## Slide 13
Corridor
Intersection
Notes: The corridor will separate into several parts, parts are roads, and parts are bridges. The middle part is the bridge, others are roads.
This intersection need to add some other types, as the ramps and interchanges.

## Slide 14
Supports
Notes: Here are two types of ending supports. The I-Beam or box-girder are supports on here. And the other end is connecting the road.

## Slide 15
Supports
Notes: In the urban elevated bridge, the bottoms of the bridge support will usually are small, like this. Because there are some other roads under the elevated bridges.

## Slide 16
Supports
Notes: If the bridge deck is wider, these types supports may be choose. Here are the supports of Railway Bridge in the above picture. The picture below is the bridge across the sea.

## Slide 17
Supports
Notes: Another type of supports.

## Slide 18
Foundation
Notes: Foundation and piles. The piles are produced in the factory, and transported to the location and then machine drive piles into the earth. The size and types of foundation depend on the geological conditions.
There are two kinds of piles distribution modes.

## Slide 19
Modeling
Notes: All the models are complete. In this picture, the I-Beam, the slab and the road section are continuous. The supports, the foundation and the piles are independence.

## Slide 20
Structure
Analysis
Notes: When design the bridge section, the supports and the foundations, the engineer will do some structure analysis with the 3D model.
If necessary, we can provide the interface, and output the 3d model of the bridge. So that some other Finite Element Analysis software (as ANSYS, ADINA) and other bridge software (as Midas Bridge, Lucas) can use the model to do the structure analysis.

## Slide 21
Drawings
Reports
Notes: And then designer can use Civil3D to output the drawings and Reports.

## Slide 22
Overview
Continuous Truss Bridge
Arch Bridge
Suspension Bridge
Cable-stayed Bridge
Bridge
Section
Supports
Foundation
Corridor
Intersection
Notes: These three parts are newly added, Bridge section, Supports, Foundations. And we need to improve the Corridor and Intersection.
After that we can model the Truss bridge in Civil 3D. If add more structure types, we can model all of the bridge types.

## Slide 23: Product Portfolio

## Slide 24: Q & A